## Slide 1: Inverted Pendulum

## Slide 2: Inverted Pendulum
A control system benchmark historically used in feedback control engineering.
A pole affixed to a cart via a joint which allows movement along a single axis. The cart is able to move along a track of fixed length.

## Slide 3
A trial typically begins with the pole off-center by a certain number of degrees.
The goal is to keep the pole from falling over by moving the cart in either direction, without the cart falling off either edge of the track.

## Slide 4: Architecture
Server:
Controller
Client:
(Java Applet)
Sensor
Actuator
Physics
UI
Updating
Socket
Communication

## Slide 5
ControlServer.java
  Wait for client’s connection
  Receive the measurement data from the sensor
  Calculate the force to be applied on the cart
    Currently it only consider the pole angle to calculate the force

## Slide 6
Client.java
  Main class for the client Applet
  Takes simulation parameters from the user
  Connect to the server
  Start the four threads on client
Physics.java
  Contains the physics data of the simulation environment
  Simulate the physical process
Pendulum.java
  Contains all the physics parameters of one inverted pendulum (mass, dimension, position …)

## Slide 7
UpdatingUIThread.java
  According to the data in Physics, update the image in the user interface
Sensor.java
  Take measurements on Physics
  Send data to controller
  Currently measures pole angle, pole angle derivate, cart position, cart position derivate
Actuator.java
  Once receive the data from the controller, update the force applied in Physics

## Slide 8: Parameters for simulation
Simulation Speed
  the ratio of simulation clock's speed over the real time clock speed
Simulation step size (in simulation second)
  the size of each step in this time-driven simulation
Sensor Type
  Time-Based sensor or Event-Based sensor
Sensor sampling rate (per simulation second)
  samples the sensor will measure per simulation second
Threshold for the event based sensor

## Slide 9
To Compile:
  javac *.java
To Run:
First, run the controller (server)
  java ControlServer
Second, Run the client (Applet):
  appletviewer Client.java

## Slide 10
To solve the “java.security.AccessControlException”:
  Add a “.java.policy” file in your home directory
  Add the following policy in the “.java.policy”:
  grant {
  permission java.net.SocketPermission
  “127.0.0.1:25533”,
  “connect, resolve”;
  };